## Slide 1: A Review of Thermal IR Imaging
Ellis Freedman
Serious Science, LLC
November 7, 2022

## Slide 2: IR Imagery Provides Information Unavailable in Visible Imagery
Heat loss or suppression
Short term variations over time
Power generation or activity
Hidden or covert activities
Easy water detection
Absolute temperature estimates
Vegetation evapotranspiration

## Slide 3: Heat Loss
Heat Vents
Prison
Temperature estimates from the image and weather data enable the estimation of BTU loss
(All images courtesy of Stockton Infrared Thermographic Services (www.stocktoninfrared.com)

## Slide 4: Hidden Activity
Underground steam pipes
(All images courtesy of Stockton Infrared Thermographic Services (www.stocktoninfrared.com)

## Slide 5: Power Generation
Hot spots on a high voltage transmission line
(All images courtesy of Stockton Infrared Thermographic Services (www.stocktoninfrared.com)

## Slide 6: Otherwise, Non-Visible Activity
Entrance Lights
Office Activity
Empty Stadium
(All images courtesy of Stockton Infrared Thermographic Services (www.stocktoninfrared.com)

## Slide 7: Temporal Activity
Truck Depot
Spots where trucks used to be
Current trucks
Truck with idling engine
Temperature estimates from the image, surface models, and weather data allow the
derivation of the time since the vehicle left
(All images courtesy of Stockton Infrared Thermographic Services (www.stocktoninfrared.com)

## Slide 8: Open Water Detection and Tracking
Stream winding through housing developments and under roads
(All images courtesy of Stockton Infrared Thermographic Services (www.stocktoninfrared.com)

## Slide 9: Lake Anna, VA Power Plant
Thermal IR sees the warm water generated by the cooling of the nuclear power plant

## Slide 10: New Orleans, LA
Landsat ETM+ Pan Band (Band 8)
Landsat ETM+ Thermal Band (Band 6)

## Slide 11: New Orleans, LA Before and After Hurricane Ida

## Slide 12: Evapotranspiration
The rate at which plant life loses water through evaporation or soil drainage
Vitally important for agriculture in light of climate change
Traditionally done with a lysimeter
  Plants are kept in a container, water drainage is measured and the plant and soil weight is measured over time
Wide area measurements can be performed with remote readings of absolute temperature

## Slide 13: Land Surface Temperature Map of Seattle and Environs

## Slide 14: Crop Stress in Sacramento

## Slide 15: Evapotranspiration Stress on Crops in Costa Rica

## Slide 16: Day Night Variations
Water generally appears cooler in the daytime thermal images and warmer in nighttime imaging.
Trees generally appear cooler during the day and warmer at night.

## Slide 17: Diurnal Temperature Variation
Middleton (WI), USA
Daytime
Nighttime
Paved areas appear relatively warm during the day and night. Pavement heats up quickly and to higher temperatures than the surrounding areas during the day and loses heat relatively slowly at night.

## Slide 18: What IR Imagery Isn’t
A spatial or visual competitor for visible imagery
  IR senses thermal phenomenology in a contextual format
  It can be registered, overlaid and sharpened with visible images to provide better context, geospatial and geodetic accuracy
  High resolution panchromatic is > 20X better resolution
    In general, civil/scientific imagery is useful for thematic or climatic evaluations, not for sensing most manmade objects

## Slide 19: Image Comparison Under Different Light Wavelengths
(a) UV light, (b) visible light, (c) SWIR light, (d) MWIR light

## Slide 20: The Equations for Thermal IR Are Similar to Those for Visible
GSD, resolution, etc. are the same
Different detectors and optics are used
  Some are photoelectric, as in the visible
    Instead of silicon, they can be made of mercury/cadmium/tellurium (MerCad), Indium/ Antimonide (InSb) or indium/gallium/arsenic (InGaAs) depending upon wavelength
  Some are not (microbolometers, pyrometers, etc.)
    Bolometers change resistance with temperature and have slower responses than other sensors.
      These are used in non-contact thermometers
  Glass and many plastics are opaque to thermal IR
    Need more exotic materials, like germanium or zinc selenide

## Slide 21: IR Requires Different Materials for the Optics
Thermal

## Slide 22: Determining Temperature Remotely Requires Knowledge of the Target Emissivity
Simplistically, if temperature is related to sensed radiance by,
then a 1% error in emissivity creates a 1.4F error in temperature.
Variability of Skin Emissivity Causes Significant Errors in Temperature
Clean Hands, Left and Right
Clean Hand vs. Hand with Ultrasound Gel

## Slide 23: Everything Radiates
Typical Thermal Bands
Average temperature of the earth is 287K.
That’s why most thermal cameras are sensitive in the range of 8um to 14um.

## Slide 24: How Greenhouse Gases Increase the Earth’s Temperature
20um
10um
5um
Upward Flux
∆ Upward Flux

## Slide 25: Thermometry vs. Radiometry
Radiometry is the measurement of the radiance (brightness) of a large area.
Thermometry is the measurement of the temperature of an object.
For each, there are absolute and relative measurements.
  Absolute radiometry or thermometry is the quantitative measurement of something on an absolute scale
    E.g. 98.6F, not warmer than something else.
  Relative radiometry or thermometry is the quantitative measurement of the difference between one object and another in the same or different scene
    E.g. water near a reactor in a cooling pond is 2.2C than water at the far end of the pond.

## Slide 26: Absolute Temperature Estimates
Absolute temperature measurements are not necessary for detection of activity
It is necessary for quantitative evaluations
  BTUs
  Power loss estimates
  Time since a vehicle has moved
Absolute temperature requires absolute radiometric calibration

## Slide 27: What is Calibration?
If A = B and B = C, then A = C
Blackbody calibrator with known temperature
Thermal Camera
Mirror
If a camera produces the same pixel values when looking at an object with an unknown temperature as when looking at an object with a known temperature, then the unknown temperature is the same as the known temperature.
Calibration is done periodically to account for changes over time.

## Slide 28: Absolute Temperature Calibration Requires a Combination of Things
On-board blackbody calibrator (i.e. a calibrator built into the camera)
Vicarious ground calibration
Accurate accounting of all thermal radiance sources, such as nearfield (self emission from telescope/sensor) calibration
  If a photoelectric detector senses heat, and the inside of the camera is warm, the total power on the detector will create a bias and increase the noise
  Microbolometers can display bias, but don’t suffer from additional noise.

## Slide 29: Potential Sources of Revenue
Detection and assessment of power generation and transmission problems
  Problem power lines and transformers will be highlighted
Detecting the activity of vehicles and aircraft
  Parking lot and airport activity
    Are mall customers continuously shopping or did the mall only see activity early in the day?
  Which cars and aircraft are running their engines?
Large scale estimation of energy efficiency in large buildings and factories
Determination of nighttime activity vs. daytime
Mapping of underground steam pipes and other activities
Theft of natural gas
Easier mapping of rivers, streams flooding and runoff
Rapid and detailed mapping of fires
Monitoring of illegal burn exhausts
Animal and human detection and location
Military, security and intelligence
Crop improvement

## Slide 30: Summary
Thermal imagery has valuable utility for many missions
  It can be combined with other sources of imagery to provide a better GIS solution
It provides information unavailable from visible cameras, but at lower resolutions.
Equations for the design and performance of thermal cameras are similar to those of other cameras, but require some additional information.
Well established technologies are available for the cameras.